## Slide 1
IEEE TCAS-I 2024
Throughput Optimisations
in CNN Inference Engine SV Implementation
Memory-Sharing & Data-Reusing Architecture — 864 PEs @ 3.85 GHz | 6.65 TOPs
6.65 TOPs
Peak Throughput
864 PEs
Array Size
3.85 GHz
ASIC Clock
3.68×
vs State-of-Art
KPU · KPC · Line Memory · PE Core · IEC · CU

## Slide 2
Architecture at a Glance
Where each throughput optimisation lives in the design
IEC
(Controller)
KPC
(Kernel
Controller)
Line
Memory
×32
PE Core
×864
(MAC+Pool)
CU
(Classify
Unit)
→ One-cycle reset pulses
→ Combinational last-iter detection
→ done_interrupt vs polling
→ Next_Stride gated in LOAD
→ Wr_Rr 2-bit packed bus
→ 3-bit minimal load_cnt
→ WAG/RAG clock-gating
→ Output buffer collapsed
→ Circular WAG wrap
→ input_reg stride-gated
→ Weight Dout zeroed when idle
→ Psum column chaining
→ Subtractor comparator
→ Bare up-counter CNG
→ Self-terminate after N
Key insight: every optimisation either eliminates idle switching activity or removes pipeline stalls

## Slide 3
KPC — Kernel Processing Controller
Throughput Optimisations in Control Signal Distribution
Next_Stride Gating
In LOAD state, all 32 Next_Stride wires are forced to zero via generate block:
assign Next_Stride[r] =
(state==COMPUTE) ?
stride_req[r] : 1'b0;
Prevents stray pulses from triggering 32 line-memory RAGs simultaneously during weight loading — stops spurious read-pointer corruption and eliminates 32 toggling outputs.
⚡ 32 simultaneous spurious RAG triggers eliminated per stray pulse
Wr_Rr 2-bit Packed Bus
Write_Selector and Read_Selector are packed into a single 2-bit bus:
Wr_Rr = 2'b10 → Write
Wr_Rr = 2'b01 → Read
PE decodes with free bit-selects:
WE = Wr_Rr[1]
RE = Wr_Rr[0]
Halves control-signal fanout into all 864 PEs. Decode is a single bit-select — zero logic gates.
⚡ 1 728 fewer routed wires into PE array (864 PEs × 2 signals saved)
Minimal load_cnt Width
Weight-loading counter declared at minimum bit-width:
logic [Z_Bit_Width-1:0]
load_cnt; // 3 bits for Z=8
load_done registered in always_ff, not combinational (load_cnt==Z-1), to eliminate glitch at wrap boundary that would falsely trigger all downstream logic.
⚡ 3-bit counter inferred vs over-provisioned wide counter. Zero glitch on done.

## Slide 4
Line Memory — 32 Instances
Clock-gating and output-buffer elimination for maximum energy-throughput efficiency
WAG / RAG Independent Clock-Gating
WAG advances only when Write_Selector is asserted.
RAG base update only when Read_Selector && Next_Stride.
During computation: WAG FFs frozen
During loading: RAG FFs frozen
Both idle simultaneously is the common case — majority of clock cycles, both address registers draw zero dynamic power.
Circular WAG Wrap — No Subtractor
Wrap expressed as ternary, not comparator:
(wag_addr == A_Bit_Width'(A-1))
? '0 : wag_addr + 1
Synthesiser maps to single carry-chain equality check. A general subtractor-based comparator (wag_addr >= A-1) would require full adder logic.
Output Buffer Collapse — 864 Registers Saved
Paper spec: n k-bit output registers + n:1 mux per line memory.
SV implementation collapses to single assign:
assign O_packed[p*K +: K] =
Read_Selector
? mem[(read_base +
A_Bit_Width'(p)) % A]
: '0;
Saving per line memory: 27 registers
Total saving: 27 × 32 = 864 registers
Trade-off: slightly wider address arithmetic path — justified because register-array area >> adder area at 16-bit data width.
⚡ 864 registers eliminated
⚡ 1 carry-chain vs subtractor

## Slide 5
PE Core — 864 Instances
Switching-activity reduction, port minimisation, and MAC idle-gating across 864 PEs
input_reg Stride-Gated (~87% toggle reduction)
Input feature register only clocks on Stride_Request:
else if (Stride_Request)
input_reg <= I_sel;
For z=8 filter depth, register clocks 1-in-8 cycles. Vs. clocking every cycle → ~87.5% switching reduction across all 864 PE input registers.
Weight Dout Zeroed When RE=0
Async-read weight memory output explicitly zeroed:
wire signed [K-1:0] Dout =
RE ? wmem[RA] : '0;
Without this, stale weight data continuously drives the multiplier operand. With it, the multiplier input is constant-zero when idle — eliminating majority of its internal switching.
R6_r_Delta 7-bit Packed Port
3 control params packed into 1 port:
wire R6 = R6_r_Delta[6];
wire r_val = R6_r_Delta[5:3];
wire Delta = R6_r_Delta[2:0];
Saves 2 signals × 864 PEs = 1 728 fewer routed wires.
RA Resets on Stride_Request
Read address reuses existing signal:
if (rst || Stride_Request)
RA <= '0;
No separate reset pulse needed. Signal reuse = fewer distinct control lines for timing closure.
Psum Column Chaining
Bias enters only column j=0; all other columns chain previous Psum:
assign b_w = (j==0)
? BIAS_Bus_packed[...]
: psum_packed[prev_col];
27-stage accumulator with zero extra adder hardware.

## Slide 6
IEC — Inference Engine Controller FSM
Zero-cycle wasted transitions, interrupt-driven handshake, combinational boundary detection
S_IDLE
S_CONFIG
S_LOAD
S_COMPUTE
S_LAYER_SWITCH
S_CLASSIFY
S_DONE
One-Cycle Reset Pulses
kpu_rst and cu_rst deasserted at top of every always_ff:
kpu_rst <= 1'b0;
cu_rst <= 1'b0;
Only specific states reassert them. A held reset keeps all 864 PE registers + CU registers clamped to zero — constant-zero drive wastes energy every cycle it is held.
done_interrupt vs Status Polling
Registered interrupt output instead of polling a status register:
→ ARM processor sleeps during inference
→ Wakes only on interrupt assertion
Paper's real-world test explicitly wires interrupt between processing system and inference engine (AXI-lite registers not polled).
layer_config_ack — Single-Cycle Handshake
IEC asserts ack for exactly one cycle on valid config capture.
Processor watches for pulse — no busy flag polling loop.
Reduces cycles wasted in config handshake to the absolute minimum (1 cycle).
l_is_FClast & last_iter — Combinational
wire l_is_FClast =
(r_layer == r_FClast);
wire last_iter =
(iter_cnt == r_nl - 1'b1);
Evaluated from already-registered values — FSM branches in same cycle last iteration completes. Zero wasted cycles at layer boundaries.
kpu_valid Direct Tap
assign kpu_valid =
kpu_inst.load_done;
Directly reads internal KPU signal. Saves one FF and eliminates one pipeline cycle lag between KPU signalling ready and IEC acting on it.

## Slide 7
CU — Classify Unit
Hardware-efficient argmax: subtractor comparator, bare counter, dual-path zeroing
DSR Zero-Forces Both Output Paths
Both output paths always driven to defined value:
l == FClast → AC_to_ACSU=0,
valid_to_CUC=0
l != FClast → AC_out=0,
valid_out=0
Neither ACSU nor IEC ever sees floating or stale bus — no undefined switching.
ACSU: Subtractor Sign-Bit Comparator
Replace dedicated comparator with:
wire signed [K-1:0] cmp =
ACi - ACMax;
wire update =
en && AC_valid && !cmp[K-1];
Sign bit of subtraction = ACi > ACMax.
Synthesis: single 16-bit subtractor, MSB tapped. Zero extra comparator gates.
class_done Registered (Anti-Glitch)
cn_reached fires combinationally when
CN_count == N, but class_done
committed to FF on next clock edge.
Prevents glitch on result_valid in DSR from propagating to IEC's S_CLASSIFY → S_DONE mid-cycle.
Bare Up-Counter CNG
Class numbers 0…N-1 are simply the counter value.
No one-hot, no priority encoder, no LUT.
For N=1000: conventional design needs 1 000 decode gates; here, just a 10-bit counter — 2 orders of magnitude fewer gates.
acsu_cng_en — 4-Condition Guard
assign acsu_cng_en =
l_is_FClast && AC_valid
&& (CN_count < N)
&& (N != '0);
N != '0 prevents zero-width counter ambiguity.
CN_count < N self-terminates after N classes — no extra controller intervention.

## Slide 8
Uninterrupted Computation Pipeline
σ = 1.0 time-efficiency: PEs are never idle during inference
Pre-fetch
r data
Compute
+
Fetch rest
Pre-fetch
next stride
Compute
next stride
→ …
TIME →
r-data Partial Prefetch
Computation starts after only r data items loaded.
Remaining data fetches happen during compute run.
PE needs new data only once per δ cycles;
line memory needs s cycles to generate new data.
δ - s cycles available for background DRAM fetch.
Vertical Stride Data Reuse
Top α-s rows of PEs re-routed to line memories that held their subsequent PE rows in previous stride.
Only s new line-memory rows fetched per stride.
Each input item reused up to z(α-s)² MAC ops.
Each filter weight reused (A-s)² MAC ops.
Warmup Formula: Z + N_PE + 4
The combinational adder tree (no pipeline register) keeps the warmup formula clean:
warmup = Z + N_PE + 4 cycles
Adding a pipeline register would add a cycle to this formula and would require 21 extra FFs for the 16-bit×(K+5)-wide accumulation bus.

## Slide 9
Summary: All Throughput Optimisations
Module
Optimisation
Mechanism
Primary Benefit
KPC
Next_Stride gated in LOAD
generate assign with state guard
Prevents 32 simultaneous spurious RAG triggers
KPC
Wr_Rr 2-bit packed control bus
Bit-select decode in each PE
1 728 fewer routed wires across PE array
KPC
Minimal load_cnt width + FF done
Z_Bit_Width-bit counter; registered done
Minimal counter + zero glitch on wrap
Line Mem
WAG/RAG independent clock-gating
if(selector) guard on address FFs
Both address registers frozen when unused
Line Mem
Output buffer collapse (−864 regs)
Single assign with modulo addressing
864 registers eliminated vs paper spec
Line Mem
Circular WAG wrap (no subtractor)
Ternary vs comparator
Single carry-chain equality, no adder
PE Core
input_reg stride-gated (−87% toggle)
Clock enable on Stride_Request only
~87.5% switching reduction per PE input reg
PE Core
Weight Dout zeroed when RE=0
wire Dout = RE ? wmem[RA] : '0
Multiplier input constant when idle → no switching
PE Core
R6_r_Delta 7-bit packed port
Bit-select decode; 3 params in 1 port
1 728 fewer PE control wires routed
PE Core
RA resets on Stride_Request (reuse)
if(rst || Stride_Request) RA <= '0
No separate reset signal; fewer control lines
PE Core
Psum column chaining (bias at j=0)
27-stage chain via existing MAC accum path
27-deep accumulation with zero extra adders
PE Core
Adder tree combinational (no reg)
always_comb final 32-row sum
Clean warmup formula; saves 21 FFs
IEC
One-cycle reset pulses (kpu_rst, cu_rst)
Deassert at always_ff top; reassert per state
Zero constant-zero drive energy waste
IEC
done_interrupt vs polling
Registered interrupt to ARM processor
CPU sleeps during inference; wakes on interrupt
IEC
layer_config_ack single-cycle pulse
1-cycle assertion on config capture
Minimum config handshake latency
IEC
Combinational last_iter & l_is_FClast
wire from registered values
Branch in same cycle iteration completes
IEC
kpu_valid direct internal tap
assign kpu_valid = kpu_inst.load_done
Saves 1 FF; eliminates 1-cycle pipeline lag
CU
DSR zero-forces both output paths
Both paths always driven to defined value
No floating/stale bus; no undefined switching
CU
ACSU subtractor sign-bit comparator
wire update = !cmp[K-1]
Single 16-bit subtractor; MSB tapped; no CMP gate
CU
class_done registered (anti-glitch)
FF captures cn_reached one cycle later
No mid-cycle glitch on S_CLASSIFY→S_DONE
CU
Bare up-counter CNG
10-bit counter value = class number
~1 000 decode gates eliminated for N=1 000
CU
acsu_cng_en 4-condition guard
N!=0 guard + CN_count<N self-termination
Self-terminating after N; no extra controller

## Slide 10
Implementation Results & Conclusion
Cumulative payoff of all SV throughput optimisations
6.65 TOPs
ASIC Peak Throughput
(28nm FD-SOI)
3.85 GHz
ASIC Clock Frequency
σ = 1.0
Time Efficiency
(PEs never idle)
3.68×
Throughput vs
State-of-Art [21]
21.8×
Energy Efficiency
vs [11]
Clock-Gating at Every Level
WAG/RAG frozen when unused. input_reg gated on Stride_Request. Weight Dout zeroed when RE=0. kpu_rst/cu_rst pulsed not held. Total: majority of flip-flops draw zero dynamic power on most cycles.
Port & Wire Count Reduction
Wr_Rr 2-bit bus and R6_r_Delta 7-bit packed port together eliminate 3,456 routed wires across the PE array. Simpler interconnect = faster timing closure and lower routing congestion.
Hardware Collapsed to Arithmetic
Output buffer → single modulo assign (−864 regs). Comparator → subtractor sign-bit (−1 CMP gate). CNG → bare counter (−~1000 decode gates). WAG wrap → ternary (−subtractor). Each saves area without losing throughput.
Zero-Stall Pipeline Discipline
Combinational last_iter / l_is_FClast ensures FSM branches with zero wasted cycles at layer boundaries. One-cycle ack handshake. Direct kpu_valid tap eliminates one pipeline lag. Warmup = Z + N_PE + 4 cleanly.
Islam et al., 'Energy-Efficient and High-Throughput CNN Inference Engine Based on Memory-Sharing and Data-Reusing for Edge Applications,' IEEE TCAS-I, Vol. 71, No. 7, July 2024

## Slide 11
ASIC
Physical
Implementation
Cadence Innovus — 45nm
CNN_Inference_Engine
Clock: 10 ns | VDD: 0.9 V
116 MHz
Max Achievable Freq
69.77 mW
Total Power (45nm)
Physical Design Flow
1
Floorplan + Place
Density: 60.0% → 66.0%
Done
2
preCTS timeDesign
WNS = 0.000 ns | 0 violations
Clean
3
CTS + Hold Fix
WNS = 0.000 ns | 0 violations
Clean
4
postCTS timeDesign
WNS = +1.399 ns | 0 setup violations
Clean
5
Hold Analysis
WNS = +0.046 ns | 0 hold violations
Clean
6
Route + Congestion
H: 0.00% | V: 0.00% overflow
0% OvF
7
Power Analysis
Voltus static @ 200 MHz activity model
69.77mW
8
GDS Export
Final layout complete
Done

## Slide 12
Timing Closure Results
Setup & Hold — MMMC OCV | 45nm | CNN_Inference_Engine | Clock: 10 ns (100 MHz target) | All reg2reg paths: 275,000
Max achievable frequency: 1 / (T_clk − WNS) = 1 / (10 ns − 1.399 ns) = 1 / 8.601 ns ≈ 116.3 MHz (0 setup violations, 0 hold violations)
Final Setup — postCTS (10 ns clock)
Metric
all
reg2reg
default
WNS (ns)
+1.399
+1.399
+3.577
TNS (ns)
0.000
0.000
0.000
Violating Paths
0
0
0
All Paths
275k
275k
82,629
Final Hold Analysis (10 ns clock)
Metric
all
reg2reg
default
WNS (ns)
+0.046
+0.046
+0.415
TNS (ns)
0.000
0.000
0.000
Violating Paths
0
0
0
All Paths
275k
275k
82,616
DRV Summary (postCTS)
DRV Check
Real Nets (terms)
Worst Violation
Status
max_cap
0 (0)
0.000
PASS
max_tran
0 (0)
0.000
PASS
max_fanout
0 (0)
0
PASS
max_length
0 (0)
0
PASS
All DRV checks PASS | Complete timing closure — setup, hold, and design rules all satisfied

## Slide 13
Congestion, Density & Power Analysis
Cadence Voltus static power + Innovus reportCongestion | 45nm | VDD = 0.9 V
Routing Congestion
H Overflow: 0 nets (0.00%)
V Overflow: 0 nets (0.00%)
Hotspot area (norm.): 0.00
Usage H: 10.1% V: 13.2%
All GCells at remain≥5
Cell Density Across Flow Stages
Post-Place (prePlaceOpt)
59.995%
preCTS (after routeDesign)
66.02%
postCTS (after optHold)
65.453%
Cadence Voltus Static Power Report — Total: 69.77 mW @ 0.9 V | 775,355 instances
46.18 mW
Internal (66.2%)
23.54 mW
Switching (33.7%)
0.049 mW
Leakage (0.07%)
69.77 mW
Total (100%)
Group
Internal (mW)
Switching (mW)
Leakage (mW)
Total (mW)
%
Sequential
22.46
1.552
0.013
24.02
34.43
Combinational
20.40
17.24
0.036
37.67
54.00
Clock (Comb.)
3.322
4.753
0.001
8.075
11.57

## Slide 14
FPGA Implementation — Exact vs Optimised
Xilinx ZCU102 Zynq UltraScale+ | Fixed-point 16-bit | Frequency at 0-slack (maximum achievable)
LUTs
Exact Model
81,178
Optimised
83,783
▲ +3.2%
Slight increase from packed control buses
Flip-Flops
Exact Model
36,601
Optimised
38,903
▲ +6.3%
Additional pipeline registers for optimised flow
Power
Exact Model
1.046 W
Optimised
1.060 W
▲ +1.3%
Negligible — within measurement noise
Frequency
Exact Model
59 MHz
Optimised
81 MHz
▲ +37.3%
Max freq at 0 slack — core throughput gain
Throughput Gain
Optimised: 81 MHz vs Exact: 59 MHz → 37.3% higher clock frequency at marginal area cost (+3.2% LUTs, +6.3% FFs)
Power delta (+1.3%) is within measurement variation — effectively identical power consumption for 37% throughput gain

## Slide 15
Power Analysis — Cadence Voltus
Static power | 45nm GPDK | VDD = 0.9 V | 775,355 instances | Sequential activity = 0.2 | Primary input activity = 0.2
69.77 mW
Total Power
46.18 mW
Internal (66.2%)
23.54 mW
Switching (33.7%)
0.049 mW
Leakage (0.07%)
Power by Functional Group
Group
Internal
(mW)
Switching
(mW)
Leakage
(mW)
Total
(mW)
%
Sequential
22.460
1.552
0.013
24.020
34.43
Combinational
20.400
17.240
0.036
37.670
54.00
Clock (Comb.)
3.322
4.753
0.001
8.075
11.57
Macro / IO
0
0
0
0
0.00
Power Distribution
Combinational
54%
Sequential
34.43%
Clock
11.57%
Clock Network Power (clk) — Period: 10 ns | Toggle: 200 MHz
Internal (mW)
Switching (mW)
Leakage (mW)
Total (mW)
% of Chip Power
3.322
4.753
0.001
8.075
11.57%
Highest average power instance: kpu_inst/PE_ROW[5].PE_COL[13].pe_inst (CLKBUFX4) = 1.147 µW | Total cap: 2.044 nF